## Slide 1
Pure Shift NMR
    Tutorial, EUROMAR 2018
Gareth Morris
NMR Methodology Group
University of Manchester

## Slide 2
The History: What ? Why ? Who ? When ? How ?
The Mechanics
Some Applications Some Problems
Pure Shift NMR

## Slide 3
What Is Pure Shift NMR?
A pure shift spectrum is one in which peak positions are determined solely by chemical shifts
  , but …
… in spectra of systems with homonuclear couplings, a perfect pure shift spectrum is an unattainable ideal: all we can do is to approximate it as closely as possible. Strong coupling sets fundamental limits on our ability to distinguish between coupled spins; and practicalities usually force us to compromise between sensitivity and spectral purity. We want methods that are general, robust, linear …

## Slide 4
The History: What ? Why ? Who ? When ? How ?
The Mechanics
Some Applications Some Problems
Pure Shift NMR

## Slide 5
Chart: 
| 1953.0 | 1955.0 | 1958.0 | 1962.0 | 1964.0 | 1966.0 | 1969.0 | 1971.0 | 1974.0 | 1976.0 | 1978.0 | 1979.0 | 1987.0 | 1993.0 | 1995.0 | 2000.0 | 2010.0
 | 30 | 40 | 60 | 100 | 200 | 220 | 270 | 300 | 360 | 400 | 470 | 500 | 600 | 750 | 800 | 900 | 1000
Magnet Development: Proton Resonance Frequency by Year
Chart: 
| 1953.0 | 1955.0 | 1958.0 | 1962.0 | 1964.0 | 1966.0 | 1969.0 | 1971.0 | 1974.0 | 1976.0 | 1978.0 | 1979.0 | 1987.0 | 1993.0 | 1995.0 | 2000.0 | 2010.0
 | 30 | 40 | 60 | 100 | 200 | 220 | 270 | 300 | 360 | 400 | 470 | 500 | 600 | 750 | 800 | 900 | 1000
Introduction of superconducting magnets
Maximum commercially available spectrometer field as a function of year, on linear (left) and log (right) scale
MHz
MHz
?
?

## Slide 6
Is High Temperature Superconductivity the Answer?

## Slide 7
The History: What ? Why ? Who ? When ? How ?
The Mechanics
Some Applications Some Problems
Pure Shift NMR

## Slide 8
1962: Richard Ernst’s PhD project …
“… My own work dealt with the construction of high sensitivity radio frequency preamplifiers … on the theoretical side, I was concerned with stochastic resonance … I tried in particular to design a scheme of homonuclear broadband decoupling to simplify proton resonance spectra. By applying a stochastic sequence with a shaped power spectral density that has a hole at the observation frequency, all extraneous protons should be decoupled without perturbing the observed proton spin. The theoretical difficulties were mainly concerned with the computation of the response to nonwhite noise. Experiments were not attempted at that time, we did not believe in the usefulness of the concept anyway, and I finished my thesis in 1962 with a feeling like an artist balancing on a high rope without any interested spectators.”
Richard Ernst, Nobel autobiography (1991)

## Slide 9
J Chem Phys 64, 4229 (1976)
1976: 45° Projection of a 2D J Spectrum
Projecting the 2DJ spectrum of a weakly coupled spin system at 45° to the F2 axis generates a pure shift spectrum, but only if it is the absolute value spectrum that is projected (which loses most of the resolution gain)

## Slide 10
J Magn Reson 35, 167 (1979)
1979: Constant-Time Evolution
Varying t1 maps out an FID that only depends on chemical shift, but
signal amplitudes oscillate as a function of T
t1
T

## Slide 11
Chem Phys Lett 93, 504 (1982)
1982: BIRD
Using a BIRD sequence element that inverts only 13C-attached protons and
a hard 180° pulse at the midpoint of t1 refocuses the effects of JHH. (First example of a “J-refocused” pure shift experiment)
13C

## Slide 12
J Magn Reson 124, 104 (1997)
1997: Pattern Recognition in Symmetrised 2D J Spectra
2DJ spectroscopy with a z-filter gives cross-shaped multiplets; nonlinear pattern recognition processing converts these into a pure shift spectrum

## Slide 13
Replacing the BIRD sequence element with a selective 180° pulse in the presence of a field gradient refocuses J in thin slices of the sample.
J Magn Reson 124, 486 (1997)
1997 : the Zangger-Sterk Method
½t1
½t1
Observing only these slices gives a pure shift spectrum. (First example of “chunked” pure shift data acquisition)

## Slide 14
Magn Reson Chem 45, 296 (2007)
2007 : Anti-z-COSY
A z-filtered anti-z-COSY mixing period restricts multiplet components to those at right angles to the diagonal; filtering out cross-peaks and projecting in this direction gives a pure shift spectrum

## Slide 15
2007 : Zangger-Sterk Revisited / Pure Shift DOSY
Chem. Commun. 2007, 933 (2007)
1/sw1
Using pure shift acquisition avoids signal overlap which would otherwise lead to incorrect apparent D values.
(Updated the ZS method to use PFGs, and changed chunk timing)
0.5/sw1

## Slide 16
The History: What ? Why ? Who ? When ? How ?
The Mechanics
Some Applications Some Problems
Pure Shift NMR

## Slide 17
Pure Shift NMR: Broadband Homonuclear Decoupling
Shifts
Couplings
We need a way to separate the effects of shifts (δ) and couplings (J), e.g.
hard 180° pulse reverses effects of δ but not of J
J-refocusing reverses effect of J but not of δ, e.g. by combining “active spin refocusing” (reverse δ for chosen spins only) with a hard 180° pulse (inverts all spins)

## Slide 18
The History: What ? Why ? Who ? When ? How ?
The Mechanics:
the Zangger-Sterk experiment, J-refocusing and PSYCHE
Some Applications
Some Problems
Pure Shift NMR

## Slide 19
J-Refocusing: the Zangger-Sterk Sequence Revisited
The combination of a hard 180° pulse and a slice- and shift-selective 180° pulse leaves the active spins (within the slice) unperturbed and the passive (outside the slice or at a different shift) inverted, refocusing the J modulation of the active spins.
J Magn Reson 124, 486 (1997)
Chem. Commun. 2007, 933
J
δ
–
+
+
+
+
+
Excite
J-refocus
Acquire
Using gradient pulses to enforce CTPs cleans up results and can remove the need for a slice-selective 90°pulse

## Slide 20
Mechanics of the Zangger-Sterk Experiment
The soft and hard 180° pulses invert the passive spins, refocusing J modulation but leaving shift evolution intact
J-refocusing
J modulation is slow, so a block of data points lasting 1/sw1 << 1/J can be measured for each value of t1, building up a pure shift interferogram. (The residual effect of J is to cause weak sidebands at multiples of sw1).
t1
t2
1/sw1
Data chunking

## Slide 21
Taking the Zangger-Sterk Sequence Apart (1)
Maps out signal dependence on t1, as in a 2D experiment
The active spins experience both 180° pulses, so do not have their shift refocused
The soft 180° pulse with the weak field gradient inverts each resonance in a different thin slice of the sample
The strong gradient pulses select spins inverted by both 180° pulses, so the only signals seen are from the thin slices of sample – the “active spins”
The remaining, “passive”, spins are left inverted, so their coupling effect on the active spins is reversed – “J-refocusing”
Iz
–Iy
–Iy cos(πδt1) cos(πJt1/2)
+Ix sin(πδt1) cos(πJt1/2)
+IxSz cos(πδt1) sin(πJt1/2)
–IySz sin(πδt1) sin(πJt1/2)
–Iy cos(πδt1) cos(πJt1/2)
+Ix sin(πδt1) cos(πJt1/2)
–IxSz cos(πδt1) sin(πJt1/2)
+IySz sin(πδt1) sin(πJt1/2)
–Iy cos(2πδt1)
+Ix sin(2πδt1)

## Slide 22
Taking the Zangger-Sterk Sequence Apart (2)
In the original ZS experiment J was refocused at the end of t1. Refocusing τA = 1/(2 sw1) later means that twice as long a chunk of data can be acquired without increasing the effect of J modulation
The hard 180° pulse refocuses δ, but J continues to evolve for a time τA
τA
τB
(In practice, a few extra data points are acquired before the start of the chunk, but then thrown away, in order to avoid the distortions caused by receiver switch on and digital filtration)
The soft 180° pulse affects only one spin at a time, simply refocusing signals, so τB has no effect on shift or J evolution
The net effect is that J refocuses at a time t1 + 1/(2 sw1), at the midpoint of the chunk of data

## Slide 23
400 MHz Zangger-Sterk Pure Shift 1H Spectrum of Clarithromycin
J Am Chem Soc 132, 12770 (2010)
Pure shift spectrum
Conventional spectrum

## Slide 24
J-Refocused Pure Shift NMR: Acquisition Methods
Excite
Acq
½t1
½t1
J-refocus
1/sw1
ASR
Interferogram
(2D acquisition to build up an interferogram)
J is refocused by the combination of a hard 180° pulse and an active spin refocusing (ASR) sequence element (in the ZS experiment, a soft pulse under a field gradient) at the midpoint of t1. A pure shift interferogram is built up by incrementing t1 in steps of 1/sw1. Slow but sure.
Real-time
(acquire an FID in real time)
Excite
Acq
Acq
[
]
n
J-refocus
ASR
In real-time experiments, acquisition of a FID is periodically interrupted by J-refocusing elements. Fast, but relaxation and other effects broaden the pure shift signals.
(An intermediate alternative is semi-real-time acquisition – J Magn Reson 293, 19-27 (2018))

## Slide 25
Pulse Sequence Elements for “Active Spin Refocusing”
BIRD
BIlinear Rotation
Decoupling:
π rotation of
protons coupled
to 13C
We divide the available spins into active spins that we observe, and passive spins that we manipulate. Combining an ASR element with a hard 180° pulse refocuses the effect on the active spins of any couplings to the passive spins.
ZS
Zangger-Sterk:
slice- / shift-
selective π rotation
BS
Band-Selective
homonuclear
decoupling:
shift-selective
π rotation
PSYCHE / anti-z-COSY:
π rotation of a
fraction sin2β of spins
“double β”
(PSYCHE)

## Slide 26
Using two small flip angle β swept-frequency (chirp) pulses, with opposite sweep directions and under a field gradient, preserves only the subset of coherences (“diagonal peak” responses) that form a stimulated echo without changing frequency.
PSYCHE: Pure Shift Yielded by Chirp Excitation
Angew Chem Int Ed 53, 6990 (2014)

## Slide 27
Mechanism of PSYCHE (1)
RF
Gz
Consider two coupled spins A and X. In the presence of a field gradient, the times at which A and X are at resonance during the chirp pulses will vary with position, so we can treat each slice as experiencing a series of four small flip angle pulses β.
time
frequency

## Slide 28
RF
Gz
Mz
“Diagonal peak” responses are refocused, and survive
Mechanism of PSYCHE (2)
time
frequency

## Slide 29
RF
Gz
Mz
“Cross-peak” responses are dephased
Mechanism of PSYCHE (3)
time
frequency

## Slide 30
RF
Gz
ZQC
Zero quantum coherence pathways experience different evolution times in different slices, and average to zero
Mechanism of PSYCHE (4)
time
frequency

## Slide 31
The decoupled signal in PSYCHE ∝ 2 sin2βcos2β, the main (“recoupling”) artefact ∝ sin4β.
PSYCHE Sensitivity and Spectral Purity
ZS, 12 ms rsnob
PSYCHE
ZS, 100 ms rsnob
Normal 1H
Angew Chem Int Ed 53, 6990 (2014)
Comparing PSYCHE and ZS methods for a complex and strongly coupled region of the 500 MHz 1H spectrum of estradiol, PSYCHE offers ca. 10× more S/N for similar spectral purity. In ZS, spectral purity is determined by selective pulse bandwidth; in PSYCHE, by β. (The sensitivity of ZS methods can be improved by using multiple frequency irradiation – nemo-ZS.)

## Slide 32
Pure Shift NMR
History: What ? Why ? Who ? When ? How ?
Mechanics
Applications Problems

## Slide 33
BIRD Pure Shift NMR of Strongly Coupled Aromatics
Selecting only those protons directly bonded to 13C can lift 1H degeneracy and restore weak coupling.
Angew Chem Int Ed 50, 9716 (2011)
Normal
ZS
BIRD

## Slide 34
Chem Commun 50, 2512 (2014)
Real-time BS Pure Shift NMR of Hesperidin Diastereomers
ZS 73 min
RTBS < 2 min
Periodically inverting all except those protons within a specified frequency band – band-selective homonuclear decoupling, BASHD – suppresses the effects of couplings to protons within that band.
[
]
n
Normal 1H

## Slide 35
An 800 MHz real-time band-selective pure shift spectrum allows the enantiomeric excess induced at the end of the peptidomimetic chain to be determined reliably.
Angew Chem Int Ed 53, 151 (2014)
5.35
5.45 ppm
5.35
5.45 ppm

## Slide 36
Angew Chem Int Ed 52, 11616 (2013)
Real-Time BIRD Pure Shift HSQC
Periodic application of BIRD/180° sequence elements during data acquisition suppresses the effects of 1H-1H homonuclear couplings in real time. Unusually, pure shift here increases both resolution and sensitivity.
[
]
n

## Slide 37
Pure shift CT-nQF-COSY
2D data are acquired conventionally, with constant time t0 chosen to maximise cross-peaks. 2DFT gives an F1-pure shift nQF-COSY, which can be covariance processed to yield a double pure shift nQF-COSY spectrum.
Angew Chem Int Ed 51, 6460 (2012)

## Slide 38
500 MHz pure shift CT-3QF-COSY: flavonoids
Normal 3QF-COSY (a), CT-3QF pure shift COSY (b), and covariance double pure shift CT-3QF-COSY (c) cross-peaks for a mixture of four flavonoids in DMSO-d6; experiment time 127 min
Angew Chem Int Ed 51, 6460 (2012)

## Slide 39
Using PSYCHE J-refocusing midway through t1 in a TOCSY sequence then using covariance processing gives a completely decoupled estradiol TOCSY spectrum
2D PSYCHE
TOCSY
covariance-processed
F1-PSYCHE-TOCSY
J Am Chem Soc 136, 11867 (2014); Chem Eur J, in press; DOI: 10.1002/chem.201800524
F1-PSYCHE-TOCSY

## Slide 40
Measuring Individual Couplings: PSYCHEDELIC
Pure Shift Yielded by Chirp Excitation to Deliver Individual Couplings: in a fully decoupled 2DJ spectrum, selective pulses reintroduce just the couplings to a chosen spin or spins
N-type modulation
Angew Chem Int Ed 55, 1090 (2016)
R-type modulation

## Slide 41
PSYCHEDELIC spectrum of cyclosporin A
Applying the selective pulses to the Hα region allows all the couplings to this region to be measured without interference or overlap
Angew Chem Int Ed 55, 1090 (2016)

## Slide 42
The History: What ? Why ? Who ? When ? How ?
The Mechanics
Some Applications
Some Problems:
strong coupling, sidebands and artefacts
Pure Shift NMR

## Slide 43
180°
When Δδ is not large compared to J, transverse components of magnetization (IxSx+IySy) interact as well as longitudinal (IzSz). This causes the spin states to mix, changing the relative strengths of coherences and opening up new coherence transfer pathways.
Strong coupling
αα
ββ
αβ cosθ +
βα sinθ
βα cosθ –
αβ sinθ
αβ
βα
αα
ββ
αα
ββ
(αβ+βα)/√2
(αβ–βα)/√2
A
X
A
B
A2
180°
180°

## Slide 44
Triple Spin Echo PSYCHE 2DJ Spectroscopy
Normal (N)
Reversed (R)
Chirp pulses generate echo at start of acquisition, but dephase signals that change shift, attenuating strong coupling artefacts
PSYCHE reverses sense of J evolution
before (N) or after (R) evolution period,
allowing echo/anti-echo processing
Chem Commun 51, 15410 (2015)

## Slide 45
Triple Spin Echo PSYCHE 2DJ Spectroscopy
TSE-PSYCHE 1H 2DJ spectrum of estradiol
Chem Commun 51, 15410 (2015)
2DJ spectrum is now in pure absorption
mode, so 45° projection works fine

## Slide 46
PSYCHE
Normal 1H
TSE-PSYCHE
1D TSE-PSYCHE: Tolerance of Strong Coupling
The TSE-PSYCHE 2DJ sequence can also be used to measure 1D spectra
Chem Commun 51, 15410 (2015)
/20

## Slide 47
1/sw1 << 1/JHH
Constructing a Pure Shift FID: chunking sidebands
Successive experiments map out the decoupled signals. The residual effect of the couplings is to impose a small modulation of the assembled interferogram, with period 1/sw1, leading to small sidebands in the resulting spectrum with spacing sw1.
J Magn Reson 271, 99 (2016)
t1 = 0
t1 = 1/sw1
t1 = 2/sw1
t1 = 3/sw1
ASR
ASR
ASR
ASR

## Slide 48
Changing the Residual J Modulation Phase: principle
Varying the net J evolution delay τJ = 2(τ1 – τ3) changes the modulation phase, and hence the phases of the sideband signals. Averaging N different delays suppresses sidebands to order N–1.
τJ = 0
τJ = 1/(16 sw1)
τJ = 2/(16 sw1)
τJ = 3/(16 sw1)
τJ = 4/(16 sw1)
τJ = –1/(16 sw1)
τJ = –2/(16 sw1)
τJ = –3/(16 sw1)
Average

## Slide 49
Changing the Residual J Modulation Phase: practice
Sidebands go through 360n° phase shifts while the centreband signals are unchanged
–3/(16 sw1)
τJ
–2/(16 sw1)
–1/(16 sw1)
0
1/(16 sw1)
2/(16 sw1)
3/(16 sw1)
4/(16 sw1)
modulation phase
0
45°
90°
135°
180°
–135°
–90°
–45°

## Slide 50
ZS pure shift spectrum with sideband suppression
Ultraclean Pure Shift NMR: SAPPHIRE sideband suppression
Sideband Averaging by Periodic PHase Incrementation of Residual J Evolution allows reliable detection of signals of minor component signals
40 mM rosuvastatin (1) and 1 mM BEM (2) in DMSO-d6
Normal ZS pure
shift spectrum
Chem Commun 53, 10188 (2017)
1
2

## Slide 51
Improving PSYCHE: Saltire Pulses
Normal PSYCHE “double β” sequence element
Adding two counter-sweeping chirp pulses gives a “saltire” pulse (named after the national flag of Scotland)
Double saltire element gives four times weaker recoupling artefacts
Single saltire element gives four times weaker recoupling artefacts and improves suppression of strong coupling and ZQC artefacts
Chem Eur J, in press; DOI: 10.1002/chem.201800524

## Slide 52
Background Reading
“Pure Shift NMR Spectroscopy”, R. W. Adams, in eMagRes, Wiley, 2014, DOI: 10.1002/9780470034590.emrstm1362
“Broadband 1H homodecoupled NMR experiments: recent developments, methods and applications”, L. Castañar, T. Parella, Magn. Reson. Chem. 53, 399–426 (2015)
“Pure Shift NMR”, K. Zangger, Prog. Nucl. Magn. Reson. Spectrosc. 86–87, 1–20 (2015)
“Pure shift 1H NMR: what is next?”, L. Castañar, Magn. Reson. Chem. 57, 47–53 (2017)
“PSYCHE Pure Shift NMR Spectroscopy”, M. Foroozandeh, G.A. Morris and M. Nilsson, Chem. Eur. J in press, DOI: 10.1002/chem.201800524

## Slide 53
https://www.nmr.chemistry.manchester.ac.uk/?q=node/415

## Slide 54
Acknowledgments
Ralph Adams, Juan Aguilar,
Laura Castañar, Yingxian Chen,
Jonathan Clayden, Guilherme Dal Poggetto,
Mohammadali Foroozandeh, Peter Kiraly,
Pinelopi Moutzouri, Mathias Nilsson,
Liladhar Paudel Manchester
Steve Coombes, Andy Phillips AstraZeneca
Davy Sinnaeve Gent
Julia Cassani Mexico City
Ralph Adams, Juan Aguilar,
Laura Castañar, Yingxian Chen,
Jonathan Clayden, Guilherme Dal Poggetto,
Mohammadali Foroozandeh, Peter Kiraly,
Pinelopi Moutzouri, Mathias Nilsson,
Liladhar Paudel Manchester
Steve Coombes, Andy Phillips AstraZeneca
Davy Sinnaeve Gent
Julia Cassani Mexico City